## Slide 1
Gonioscopy
Daniel Lee, MD

## Slide 2: We are not doing enough gonioscopy…
More than 50% of patients with a glaucoma diagnosis have never had gonioscopy
1 out of 10 patients referred by other ophthalmologists with “open angle glaucoma” actually had angle closure glaucoma
Angle closure accounts for half of glaucoma blindness worldwide

## Slide 3: Why aren’t we doing it more?
It’s inconvenient and time-consuming
Patients find it uncomfortable
It’s difficult to master
Angle anatomy is confusing…
Gonioscopy is the scleral depression of the anterior segment.

## Slide 4: Total Internal Reflection
The light from the trabecular meshwork does not exit the eye
Snell’s Law
  Rays approaching the air-tear interface < 46 degrees are reflected back

## Slide 5: Gonioscopy Overcomes Total Internal Reflection
Direct Gonioscopy
  Lens is placed on the eye, replacing the air-tear interface
  Allows for “direct” or upright visualization of the angle
  Most commonly used for intra-operative visualization of the angle
    Patient must be supine
    Awkward viewing angle
  Koeppe, Barkan, and Swan Jacob

## Slide 6: Gonioscopy Overcomes Total Internal Reflection
Indirect Gonioscopy
  The angle is visualized “indirectly” through a mirror
  Able to visualize the angle with a slit lamp
    Light rays are reflected off the mirror and exit parallel to the optical axis

## Slide 7: Types of Indirect Gonio Lenses
Goldmann
  3 mirrors
  Excellent view of angle (also peripheral retina)
  Usually needs a viscous coupling agent
  Easier to use
  15 mm contact diameter
  Cannot perform indentation gonioscopy

## Slide 8: Types of Indirect Gonio Lenses
Zeiss, Posner, and Sussman
  4 mirrors
  No coupling agent necessary
  More difficult to master
  9 mm contact diameter
  Allows for indentation gonioscopy

## Slide 9: Technique
Anesthetize the eye
Position patient in slit lamp
Have patient look up
Brace upper and lower lid with fingers
Gently place gonio lens on cornea
Ask patient to look straight

## Slide 10: Technique
Minimize light going through the pupil
  Induced pupillary constriction may artificially open the angle
  Turn room lights off and keep slit beam small on dim setting
Note: When evaluating for neovascularization, it’s helpful to have high illumination.

## Slide 11: Technique
Excess light induces pupillary constriction and artificially opens the angle

## Slide 12: Technique
The gonio lens should very gently contact the corneal surface
Posterior pressure and corneal indentation will artificially open the angle

## Slide 14: Technique
Begin your examination at the superior lens = inferior angle
  Typically the most open
  The most defined pigmentation
Can go clockwise or counter-clockwise
  Just be consistent

## Slide 17: Indentation Gonioscopy
The lens diameter is smaller than the corneal diameter
Pushing posteriorly drives the lens-iris diaphragm back, which exposes the obscured angle
  Determine if angle closure is appositional or synechial
  “Double hump sign” in plateau iris

## Slide 18: Great Gonioscopy Resources