## Slide 1
Introduction to
Cataract Surgery
Christina McGowan, MD

## Slide 2: Step 1: Paracentesis
Can use different blades, including a 30-degree blade or a Supersharp blade

## Slide 3: Step 2: Intracameral Anesthetic
Preservative-free lidocaine or Epi-Shugarcaine (epinephrine with lidocaine)
  Epi-Shugarcaine maximizes pupillary dilation and iris stability
Injected through the paracentesis wound
If Trypan is used to stain the anterior capsule, it is injected after the anesthetic then irrigated out of the eye with BSS after ~10 seconds

## Slide 4: Step 3: Dispersive Viscoelastic
Injected through the paracentesis to deepen the anterior chamber for the main incision formation
Common brands:
  Viscoat (Alcon)
  Amvisc (B&L)
  Healon (J&J)

## Slide 5: Step 4: Main Wound
Typically use a 2.4 mm keratome to make a triplanar wound
Stabilize the eye using 0.12 forceps in the paracentesis wound

## Slide 6: Step 5: Iris Expansive Devices (if Needed)
Place an Malyugin ring or iris hooks, if needed, to expand the iris

## Slide 7: Step 6: Capsulorrhexis
Use a cystotome to begin the capsulotomy with a capsular flap
Use a cystotome or Utrata forceps to direct the flap along a continuous curvilinear capsulorrhexis

## Slide 8: Step 7: Hydrodissection
Use a cannula with BSS to inject a fluid wave around the lens to break cortical adhesions and mobilize the lens in the capsular bag

## Slide 9: Step 8a: Grooving
Use the sculpt setting
Judge depth of groove
  Red reflex brightens the deeper you are
  Needle thickness
    3 needle thickness centrally
    2 needle thickness in mid-periphery

## Slide 10: Step 8b: Nuclear Rotation
Torque application
  Rotate nucleus by applying pressure at most peripheral extent of groove
  Also apply pressure against densest part of remaining nucleus

## Slide 11: Step 8c: Nuclear Division – Divide & Conquer

## Slide 12: Step 8c: Nuclear Division – Horizontal Chop

## Slide 13: Step 8c: Nuclear Division – Vertical Chop

## Slide 14: Step 8d: Nuclear Removal

## Slide 15: Step 9: Cortical Removal
Irrigation/Aspiration (I/A) handpiece
Options
  Straight tip
  Angled tip: 45- or 90-degree
  Bimanual
  Curved soft silicone
Manual J-cannula if needed

## Slide 16: Step 10: Cohesive Viscoelastic
Fill the capsular bag with cohesive viscoelastic to create space for the intraocular lens

## Slide 17: Step 11: Intraocular Lens

## Slide 18: Step 12: Aspiration of Viscoelastic
Confirm that the IOL is centered within the capsular bag
Aspirate the viscoelastic from the capsular bag and anterior chamber to prevent post-operative IOP spike

## Slide 19: Step 13: Hydration of Corneal Wounds
Hydrate the main corneal incision and paracentesis incision(s) with balanced salt solution to seal the incisions
Pressurize the eye to 20-25 mmHg
Check the wounds with a Weck-Cel sponge to confirm that they are Seidel negative