## Slide 1
Biometry and Topography
Aditya Kanesa-thasan, MD

## Slide 2: Outline
Overview of biometry
Methods of biometry
IOL calculation formulas
Special cases
Addressing astigmatism
Corneal topography

## Slide 3
Overview of Biometry

## Slide 4: What is Biometry?
Biometry is measurement of the eye with the goal of determining the proper IOL power
Each biometer obtains a standard set of data for this purpose
The concept of biometry has expanded to include preoperative topography, aberrometry, and OCT of the retina to help build a surgical plan

## Slide 5: History of Biometry
When Sir Harold Ridley implanted the first IOLs, there were no IOL calculations
The first patient reportedly had a post-operative refraction of about -20D
In today’s environment, we have many IOLs available and a much higher bar for refractive outcomes following cataract surgery

## Slide 6: What is Captured?
AL (Axial Length)
ACD (AC Depth)
AD (Aqueous Depth)
LT (Lens Thickness)
WTW (White-to-White)
CCT (Central Corneal Thickness)

## Slide 7: What is Captured?
Keratometry (flat and steep K)
AL (Axial Length)
ACD (AC Depth)
LT (Lens Thickness)
WTW (White-to-White)
CCT (Central Corneal Thickness)

## Slide 8: Effective Lens Position
The ultimate goal is to predict the Effective Lens Position (ELP), where the IOL will sit in the capsular bag
You can think of this as the post-operative ACD
The position of the IOL affects its refractive power

## Slide 9
Methods of Biometry

## Slide 10: A-Scan Biometry
Previously, contact A-scan ultrasound was the gold standard
An ultrasound probe is placed on the cornea, and peaks are read for the distances from the probe
Sources of error included variable amount of pressure from the probe and variable angle of contact
Immersion A-scan biometry uses a scleral shell to submerge the eye in water so the probe does not contact the eye

## Slide 11: A-Scan Biometry

## Slide 12: Optical Biometry
Currently, most ophthalmologists use optical biometry, which is far more accurate and repeatable for measurements
Using light instead of sound allows the patient to fixate directly on a stimulus, ensuring the measurement is axial with the macula
Many measurements can be collected with tight standard deviations

## Slide 13: Optical Biometry
There are a few major machines used currently:
  Zeiss IOL Master 500
  Zeiss IOL Master 700 (uses swept source OCT)
  Haag-Streit Lenstar LS900
  Nidek AL-Scan
  Topcon Aladdin
  Oculus Pentacam AXL

## Slide 14
IOL Calculation Formulas

## Slide 15: IOL Calculation Formulas
One of the earliest IOL calculation formulas was the SRK:
  IOL power = A – 0.9K – 2.5AL
Many other formulas have been developed and tested over the years, and for many years none were superior for all eyes
Recent research has shown some of the newest formulas to be very accurate for all types of eyes
Still, only about 70-88% of eyes reach +/- 0.5D of the aim in best case scenarios

## Slide 16: IOL Calculation Formulas
Published in October 2016
Between Barrett Universal II, Holladay I, Hoffer Q, SRK/T, T2, Haigis, and Holladay 2, Barrett Universal II had lowest mean error over the entire axial length range, particularly in higher myopes

## Slide 17: IOL Calculation Formulas
Published in September 2017
Compared a large set of formulas and graphed accuracy based on axial length, keratometry, and ACD
Barrett Universal II was the best performing formula

## Slide 18: IOL Calculation Formulas
Barrett U2
Melles et al. Accuracy of Intraocular Lens Calculation Formulas.

## Slide 19: IOL Calculation Formulas
Barrett U2
Melles et al. Accuracy of Intraocular Lens Calculation Formulas.

## Slide 20: IOL Calculation Formulas
Barrett U2
Melles et al. Accuracy of Intraocular Lens Calculation Formulas.

## Slide 21: IOL Calculation Formulas
Barrett U2
Melles et al. Accuracy of Intraocular Lens Calculation Formulas.

## Slide 22: IOL Calculation Formulas
doctor-hill.com (Warren Hill, MD)

## Slide 23: IOL Calculation Formulas
Published in January 2020, included 10,930 patients
Compared Kane, Hill-RBF 2.0, Holladay 2, Barrett U2, Olsen, Haigis, Holladay 1, Hoffer Q, and SRK/T for lowest absolute error
Kane had the most eyes within 0.5D (72%), followed by Hill-RBF (71.2%), Holladay 2 (71%), and Barrett U2 (70.7%)

## Slide 24: IOL Calculation Formulas
Published in April 2021
The lowest absolute median error was achieved by the Kane formula (0.214), Hill-RBF 2.0 (0.215), and Barrett Universal II (0.218), followed by SRK/T (0.223)

## Slide 25: IOL Calculation Formulas
Published in May 2021
Hill-RBF 3.0 showed an improvement over 2.0 with decreased mean errors compared to older formulas, but not clearly superior to other modern formulas

## Slide 26: IOL Calculation Formulas
In the 2021 cataract surgery landscape, the evidence support the fact that you should only need to use a few formulas:
  Barrett Universal
  Hill-RBF 3.0
  Kane Formula
  All are readily available online and built into some biometers

## Slide 27: Barrett Universal II
Evolved from Barrett Universal I, which was developed by Dr. Graham Barrett in 1987
Based on ray tracing
The formula itself is unpublished
Uses AL, K, and ACD. LT and WTW can be added optionally for higher accuracy

## Slide 28: Barrett Universal II Calculator

## Slide 29: Barrett Universal II Calculator

## Slide 30: Hill-RBF 3.0
Initially developed as Hill-RBF 1.0, then expanded to 2.0 then 3.0 after additional datasets were added to expand the boundaries
Based on artificial intelligence regression using a radial basis function (RBF)
The formula itself is unpublished
Uses AL, K, and ACD. Gender, LT, CCT, and WTW can be added optionally

## Slide 31: Hill-RBF 3.0 Calculator

## Slide 32: Hill-RBF 3.0 Calculator

## Slide 33: Kane Formula
Based on theoretical optics and partially based on artificial intelligence
The formula itself is unpublished
Uses AL, K, ACD, and gender. LT and CCT can be added optionally for higher accuracy
Also has a built-in keratoconus option, which is highly accurate for those patients

## Slide 34: Kane Formula Calculator (+/- Keratoconus)

## Slide 35: Kane Formula Calculator (+/- Keratoconus)

## Slide 36: A Word on “A Constants”
You may have noticed that each of these formulas require an “A constant” or other such factor in order to calculate a lens power
Each lens comes with a manufacturer recommended lens constant, however there are generally accepted “optimized” lens constants and surgeon-specific lens constants
There are ways to optimize your lens constants to you but you should only do this after you have done 20-30 cases to reflect on, and each time you should only adjust it a very small amount
I personally use the optimized constants provided

## Slide 37
Special Situations

## Slide 38: Special Situations: Sulcus Placement
Most IOL formulas assume placement in the capsular bag
Placement in the ciliary sulcus without optic capture leaves the lens slightly more anterior than its position in the capsular bag (approximately 0.5mm)
To compensate for this anterior placement, you should subtract some power from most lenses, however the amount to subtract varies based on the power of the lens being placed
For optic capture of a sulcus lens, most use in the bag calculations

## Slide 39: Special Situations: Sulcus Placement
Roughly:
  Lens power less than 9: NO adjustment
  Lens power 9.5 to 17: Subtract 0.5D
  Lens power 17.5 to 28: Subtract 1D
  Lens powers above 28: Subtract 1.5D
There is a chart that goes over this relationship on doctor-hill.com

## Slide 40: Special Situations: Post-Refractive
For patients who develop cataract after corneal refractive surgery, there are several methods to determine the correct IOL formula
IOL formulas make assumptions about total corneal power based on the ratio of the anterior to posterior cornea (Gullstrand ratio) and other biometric parameters
LASIK/PRK alters the anterior cornea but not posterior cornea
RK flattens both

## Slide 41: Special Situations: Post-Refractive
ASCRS has a post-refractive calculator online that takes multiple pieces of data and gives calculations with different formulas
Helpful pieces of information include your patient’s refraction prior to LASIK/PRK, or even keratometry if they have it
There are a few “no history” methods, including Barrett True K and Pentacam, but they are improved significantly with prior data
You can access the Barrett True K and True K toric calculator on their own online

## Slide 42: ASCRS Post-Refractive Calculator

## Slide 43
Addressing Astigmatism

## Slide 44: Addressing Astigmatism
One of the major needs of modern biometry is accurate and repeatable assessment of astigmatism
This has come out of major advances in toric and toric multifocal lenses, which require these measurements in order to accurately plan treatments

## Slide 45: Addressing Astigmatism
Published in 2012
The posterior cornea is steeper in the vertical meridian and acts as a negative powered lens which contributes ATR astigmatism
The magnitude of this effect was ~0.3-0.5D ATR astigmatism

## Slide 46: Addressing Astigmatism
Published in December 2013
Analyzed toric IOL outcomes and found that WTR anterior corneal astigmatism was overestimated by about 0.5D
ATR anterior corneal astigmatism was underestimated by 0.2-0.3D

## Slide 47: Addressing Astigmatism
No longer necessary to make these corrections as these findings are now incorporated into modern toric calculators
crstodayeurope.com (Abulafia et al.)

## Slide 48: Addressing Astigmatism
crstodayeurope.com (Abulafia et al.)

## Slide 49: Toric IOL Calculation Formulas
Published in 2020
Compared Abulafia-Koch, Barrett Toric, Kane Toric, EVO 2.0, Holladay 2 with total SIA, Naeser-Savini in retrospective review
Kane Toric and Barrett Toric had the highest percentage of predicted refractions within 0.5D (65% and 59.5%, respectively)

## Slide 50: Toric IOL Calculation Formulas
The IOL Master 700 now has the capability to measure posterior corneal astigmatism and calculate total corneal power (TK)
However, some studies have shown equivalent outcomes with and without total corneal power measurements. This may require future optimization

## Slide 51
Corneal Topography

## Slide 52: Corneal Topography
Topography can be its own lecture, but in the setting of biometry and cataract planning, the main goal is to evaluate and measure corneal astigmatism
If the astigmatism is regular and the axis well defined, the patient might be a good candidate for a toric IOL or other astigmatism intervention

## Slide 53: Corneal Topography
Identify the steep axis and compare against autorefraction and glasses
Identify the magnitude of astigmatism and determine whether clinically significant
Determine if the astigmatism is regular or irregular
Look for signs of dry eye, ABMD, or other issues that can affect astigmatic readings

## Slide 54: Barrett Toric Calculator

## Slide 55: Surgically-Induced Astigmatism
This was evaluated by several surgeons including Warren Hill, who found wide variations in surgeon induced astigmatism
The variety has to do with wound architecture and corneal biomechanics, as well as the location of the wound
In vector analysis and in the absence of calculating individual SIA, a value of 0.12 was recommended, with the recognition that this is highly variable from case to case in any surgeon’s hands

## Slide 56: Angle Alpha and Angle Kappa
Angle alpha and angle kappa are important for centration of multifocal optics
Angle alpha is the distance between the visual axis and the center of the limbus (presumed center of the capsular bag)
  In biometry, this is represented as Ix and Iy for distance from iris center
Angle kappa is the distance between the visual axis and the pupil center
  In biometry, this is represented as px and py, or Chang-Waring chord

## Slide 57: Angle Alpha and Angle Kappa
cataractcoach.com (Uday Devgan)

## Slide 58: Angle Alpha and Angle Kappa
cataractcoach.com (Uday Devgan)

## Slide 59: Angle Alpha and Angle Kappa
cataractcoach.com (Uday Devgan)

## Slide 60: Angle Alpha and Angle Kappa
If angle alpha or kappa are sufficiently large, then the visual axis will be off from the natural centration of the lens in the capsular bag and/or from the center of the pupil
Different surgeons use different cutoffs, but a generally-accepted value is <0.6mm angle alpha for a diffractive multifocal
Centering the lens on the subject-fixated coaxially-sighted corneal light reflex helps to center on the patient’s subjective visual axis (typically slightly nasal)

## Slide 61: Intraoperative Aberrometry
Intraoperative aberrometry (specifically ORA by Alcon, the only current option) can be helpful for confirming biometry in the OR
The machine takes an aphakic refraction during cataract surgery, but its IOL recommendation depends the pre-operative biometry
Therefore, if you have inaccurate pre-operative biometry, then the machine will not necessarily save you
Studies comparing the two have favored preop biometry, however this is a useful adjunct in post-refractive or white cataract cases

## Slide 62
Biometry Examples

## Slide 63
IOLMaster 700 Biometry
62

## Slide 64
IOLMaster 700 Biometry
63

## Slide 65
IOLMaster 700 Biometry
64

## Slide 66
IOLMaster 700 Biometry
65

## Slide 67
IOLMaster 700 Biometry
66

## Slide 68
Barrett Toric Calculator
67

## Slide 69
Barrett Toric Calculator
68

## Slide 70
IOLMaster 700 Biometry
69

## Slide 71
IOLMaster 700 Biometry
70

## Slide 72
IOLMaster 700 Biometry
71

## Slide 73
IOLMaster 700 Biometry
72

## Slide 74
IOLMaster 700 Biometry
73

## Slide 75
IOLMaster 700 Biometry
74

## Slide 76
iTrace Topography/Aberrometry
75

## Slide 77
iTrace Topography/Aberrometry
76

## Slide 78
iTrace Topography/Aberrometry
77

## Slide 79
iTrace Topography/Aberrometry
78

## Slide 80
iTrace Topography/Aberrometry
79

## Slide 81
Autokeratometry
80

## Slide 82
Lenstar LS900 Biometry
81

## Slide 83
Lenstar LS900 Biometry
82

## Slide 84
Lenstar LS900 Biometry
83